|  | ......................... pcs. .............................. € .............................. € Integrated door closer GEZE Boxer with mechanical hold-open device, for single-action doors from 40 mm door leaf thickness; with infinitely adjustable closing force size 2 – 4 in accordance with EN 1154; guide rail with mechanical hold-open device, hold-open bracket with precise variable adjustment between 80° and 120°, hold-open position can be overridden, variable hold-open force; closing force, closing speed, back check and latching action are adjustable after installation. The closer is installed completely inside the door leaf, the guide rail can only be seen when the door is open. Up to 130 kg door leaf weight / 1100 mm door width for left and right single-action doors Colour: ( ) silver-coloured ( ) acc. to RAL |
| --- | --- |